## Slide 1: 1587: COMMUNICATION SYSTEMS 1 Wide Area Networks
Dr. George Loukas
University of Greenwich, 2015-2016

## Slide 2: Type of network by area covered
Internet
WAN
MAN
LAN
PAN
BAN
Wide Area Network
Metropolitan Area Network
Personal Area Network
Body Area Network
Local Area Network

## Slide 3: Wide Area Networks
Use local and long-distance telecommunications
Usually very high speed with low error rates
Usually follow a mesh topology
WAN
Wide Area Network

## Slide 4: Network Mesh
A mesh is a network where all nodes can send, receive and relay data
A mesh is fully connected when all nodes are directly connected to all other nodes

## Slide 5: Fully connected Mesh
4 nodes, 6 links. Is that a problem?
8 nodes, 45 links. Is that a problem?
For fully connected network:
For 50 nodes,
links

## Slide 6: Fully connected Mesh: exercises
It’s a 6-node fully connected mesh with one extra node attached to it through one link. So, 15 + 1 = 16 links.
nodes
and _____
links
If it were a fully connected mesh, it would have ____________________ links
6
9
(6 • 5)/2 =15
A network has 7 nodes. All nodes are connected with each other except for one node, which is connected to only one other node. How many links does the network have?

## Slide 7: Network Mesh
A station is a device that interfaces a user to a network
The sub-network is the connection of nodes and telecommunication links. There are three types:
A node is a device (computer,
router, …) that allows the transfer of information
Message-switched
Circuit-switched
Packet-switched

## Slide 8: Sub-network: Types
Store-and-forward
Good for broadcasting
Today completely obsolete
Example: Telex
Message-switched
Circuit-switched
Packet-switched

## Slide 9
message
message
message
propagation delay
processing
+ queuing delay
source
destination
Intermediate
node 1
Intermediate
node 2
Start sending first message
Finish sending first message
source
Intermediate
node 1
Intermediate
node 2
destination
transmission delay
Message-switched
Circuit-switched
Packet-switched

## Slide 10: Sub-network: Types
Circuit-switched
Packet-switched
A dedicated circuit (physical path) is established between sender and receiver and all data passes over this circuit.
The connection is dedicated until one party or another terminates the connection. Fixed Data Rate.
Today increasingly uncommon
Example: Telephone (PSTN)
Message-switched

## Slide 11
Data
call set up
searching for a connection
acknowledgement comes back
Circuit-switched
Packet-switched
Message-switched
source
destination
Intermediate
node 1
Intermediate
node 2

## Slide 12
Sender
Receiver
node
node
node
node
node
Circuit establishment
Information transfer
Circuit disconnection
Data
Control Signal
Control signal
Circuit-switched
Packet-switched
Message-switched
Notes: Circuit establishment –
  end-to-end connection must be established
Information transfer
  analogue voice, digitised voice or binary data
  capacity across the network is dedicated for
  even if no data is transferred
  makes the network transparent to the users
  no delays
Circuit disconnection
  control signal to disconnect

## Slide 13: Sub-network: Types
Circuit-switched
Packet-switched
Message-switched
All data messages are transmitted using suitably sized packages, called packets.
Packets contain data and a header.
No unique dedicated physical path
example: Internet
Two types: Datagrams and Virtual Circuits
Internet

## Slide 14
processing
+ queuing delay
PACKET 1
PACKET 2
PACKET 3
PACKET 1
PACKET 2
PACKET 3
PACKET 1
PACKET 2
PACKET 3
source
destination
Intermediate
node 1
Intermediate
node 2
transmission
delay
propagation
delay
Circuit-switched
Packet-switched
Message-switched

## Slide 15
Circuit-switched
Packet-switched
Message-switched
Packet transfer delay = transmission + propagation + queuing + processing
Depends on length of physical link d (m) and propagation speed is medium s (m/s).
Propagation delay = d / s
Depends on packet length L (bits) and link bandwidth R (bits/s).
Transmission delay = L / R
Depends on congestion
Depends on speed of processor (for error-checking etc.)
If the queuing delay is 4 ms, the processing delay is 1 ms, the propagation delay is insignificant, and the link bandwidth is 8 Mbps, what is the total packet transfer delay for a 1,000-byte packet over one such link?
Packet transfer delay = transmission + propagation + queuing + processing
= 1 ms + 0 + 4 ms + 1 ms = 6 ms
L = 1,000 bytes = 8•103 bits
R = 8 Mbps = 8•106 bits/s
L / R = 10-3 s = 1 ms

## Slide 16: Packet-switching: Datagrams
  Each packet carries extra overheads, e.g.
  addresses (source and destination)
  seq number etc.
Data 1
Data 2
Data 3
Circuit-switched
Packet-switched
Message-switched
Datagrams

## Slide 17: Circuit Switching Vs. Packet Switching
CALL SETUP REQUIRED
DEDICATED PHYSICAL PATH
PACKETS MAY FOLLOW DIFFERENT ROUTE
PACKETS ARRIVE ALWAYS IN ORDER
AVAILABLE BANDWIDTH IS FIXED
STORE AND FORWARD TRANSMISSION
CHARGED PER BYTE
CHARGED PER MINUTE
CIRCUIT-Switched
PACKET-Switched
Notes: Circuit
Advantages
  charges are only for the connection time
  favourable to those needing occasional short calls
  cost effective when one device is communicating for long periods.
Disadvantages
  circuit must first be set-up
  time is relatively long (several seconds)
  resulting circuit can only be used by the two connected computers
  circuits can vary in quality
  transmission rates are low - 9600 b/s to 33.6 Kb/s
  can be inefficient - a line may stand idle for most of the connection time
  many low speed links can be very expensive using circuit-switching.

## Slide 18: Packet-switching: Virtual Circuit
  Identifier (label)
  Faster switching
  No seq number required
sender
receiver
Control
Data 1
Data 2
Data 3
Control
Establishing the Circuit
Transferring information
Disconnecting the Circuit
Circuit-switched
Packet-switched
Message-switched
Datagrams
Virt. Circuits

## Slide 19: Packet-switching: Virtual Circuit
Switched virtual circuit (SVC)
  exists only for the duration of the data transfer
  For each connection, a new circuit must be created
Permanent virtual circuits (PVC)
  like leased lines, on a continuous basis
  dedicated to specific user and no-one else can use it
  no connection establishment or termination
  user of a PVC will always get the same route
Circuit-switched
Packet-switched
Message-switched
Datagrams
Virt. Circuits

## Slide 20: Circuit Switching Vs. Packet Switching
Circuit switching
  setup delay
  no other noticeable delays
Packet Switching
Virtual-circuit packet switching
  setup delay
  call acceptance response may experience delays
  data packets are queued at each node
  may experience delays - depending on load
Datagrams
  no call setup
  need to carry full address in each packet
Circuit-switched
Packet-switched
Message-switched
Datagrams
Virt. Circuits

## Slide 21: Examples of Wide Area Network protocols
ATM
Uses virtual circuit
Cell switching (similar to packet switching but uses fixed-sized 53-byte cells)
High speed and low delay thanks to the fixed cell sizes
Guaranteed QoS
Uses admission control
Frame Relay
Uses virtual circuit
Designed for speed rather than reliability
Very simple and affordable
No special reservations
MPLS
Uses virtual circuit
No congestion because bandwidth is booked in advance
Guaranteed QoS
Uses admission control

## Slide 22: Examples of Wide Area Network protocols
ATM
ADMISSION CONTROL
Users negotiate with the network regarding the length of time, type of traffic, delay, bandwidth requirements etc.
If their request cannot be met, they are denied access
Uses virtual circuit
Cell switching (similar to packet switching but uses fixed-sized 53-byte cells)
High speed and low delay thanks to the fixed cell sizes
Guaranteed QoS
Uses admission control

## Slide 24: Types of traffic
Stream traffic - lengthy and continuous
Bursty traffic - short sporadic transmissions
Maria
Lin
Good morning Lin.
Maria: Good morning Lin.

## Slide 25: Network Congestion
When a part of the network has so much traffic that individual packets are delayed noticeably
Can be caused by node and link failures; high amounts of traffic; improper network planning.
Severe congestion overflows buffers and causes packet losses

## Slide 26: Routing
Each node in a WAN is a router. Multiple possible routes.
How does a router decide where to route?

## Slide 27: Routing
Every network is essentially a weighted graph of nodes and links
The links between nodes have associated costs, such as:
  Delay
  Number of hops
  Bandwidth
  Financial cost

## Slide 28: Routing: Flooding
Least intelligent, but useful sometimes
All possible routes are tried
All nodes are visited (useful to distribute information like routing)
At least one packet will take the minimum cost route (to be used for a virtual circuit)
To avoid overwhelming the network with “undead” packets
- Impose a hop limit (the number of times a packet can be copied)
and
- When a node receives a packet, it forwards it to its other neighbours, not the one it just receive it from

## Slide 29: Dijkstra’s Least-Cost Algorithm
Finds all possible paths between two locations
Identifies the least-cost path
Finds shortest paths from given source node to all other nodes, by developing paths in order of increasing path length

## Slide 30: Example of Dijkstra’s Algorithm
E
A
C
D
F
G
B
7
3
7
3
2
7
5
2
1
3
Must already know all individual link costs
ms
ms
ms
ms
ms
ms
ms
ms
ms
ms

## Slide 31: Example of Dijkstra’s Algorithm
E (∞, -)
A
C (∞, -)
D (∞, -)
F (∞, -)
G (∞, -)
B (∞, -)
7
3
7
3
2
7
5
2
1
3
Set all distances to ∞

## Slide 32: Example of Dijkstra’s Algorithm
E (∞, -)
A
C (3, A)
D (7, A)
F (∞, -)
G (∞, -)
B (7, A)
7
3
7
3
2
7
5
2
1
3
Examine nodes adjacent to A and update distances.
Identify the nearest node that is not permanent. This is now labelled as permanent.

## Slide 33: Example of Dijkstra’s Algorithm
E (∞, -)
A
C (3, A)
D (5, C)
F (8, C)
G (10,C)
B (7, A)
7
3
7
3
2
7
5
2
1
3
Examine nodes adjacent to C that are not permanent and update distances.
Identify the nearest node that is not permanent. This is labelled as permanent.

## Slide 34: Example of Dijkstra’s Algorithm
E (8, D)
A
C (3, A)
D (5, C)
F (8, C)
G (10,C)
B (7, A)
7
3
7
3
2
7
5
2
1
3
Examine nodes adjacent to D that are not permanent and update distances.
Identify the nearest node that is not permanent. This is labelled as permanent.

## Slide 35: Example of Dijkstra’s Algorithm
E (8, D)
A
C (3, A)
D (5, C)
F (8, C)
G (10,C)
B (7, A)
7
3
7
3
2
7
5
2
1
3
Examine nodes adjacent to B that are not permanent and update distances.
Identify the nearest node. This is labelled as permanent.

## Slide 36: Example of Dijkstra’s Algorithm
E (8, D)
A
C (3, A)
D (5, C)
F (8, C)
G (9,F)
B (7, A)
7
3
7
3
2
7
5
2
1
3
Examine nodes adjacent to F that are not permanent and update distances.
Identify the nearest node. This is labelled as permanent.

## Slide 37: Example of Dijkstra’s Algorithm
E (8, D)
A
C (3, A)
D (5, C)
F (8, C)
G (9,F)
B (7, A)
7
3
7
3
2
7
5
2
1
3
Examine nodes adjacent to E that are not permanent and update distances.
Identify the nearest node that is not permanent. This is labelled as permanent.

## Slide 38: 2nd Example of Dijkstra’s Algorithm
E
A
C
D
F
G
B
7
3
7
3
11
4
3
2
4
3
Must already know all individual link costs
2
5
4
2
3
2

## Slide 39: 2nd Example of Dijkstra’s Algorithm
E (∞, -)
A (∞, -)
C (∞, -)
D (∞, -)
F
G (∞, -)
B (∞, -)
7
3
7
3
11
4
3
2
4
3
2
5
4
2
3
2
Set all distances to ∞

## Slide 40: 2nd Example of Dijkstra’s Algorithm
E (∞, -)
A (∞, -)
C (∞, -)
D (∞, -)
F
G (3, F)
B (4, F)
7
3
7
3
11
4
3
2
4
3
2
5
4
2
3
2
Examine nodes adjacent to F and update distances.
Identify the nearest node that is not permanent. This is labelled as permanent.

## Slide 41: 2nd Example of Dijkstra’s Algorithm
E (5, G)
A (∞, -)
C (∞, -)
D (∞, -)
F
G (3, F)
B (4, F)
7
3
7
3
11
4
3
2
4
3
2
5
4
2
3
2
Examine nodes adjacent to G that are not permanent and update distances.
Identify the nearest node that is not permanent. This is labelled as permanent.

## Slide 42: 2nd Example of Dijkstra’s Algorithm
E (5, G)
A (11, B)
C (∞, -)
D (∞, -)
F
G (3, F)
B (4, F)
7
3
7
3
11
4
3
2
4
3
2
5
4
2
3
2
Examine nodes adjacent to B that are not permanent and update distances.
Identify the nearest node that is not permanent. This is labelled as permanent.

## Slide 43: 2nd Example of Dijkstra’s Algorithm
E (5, G)
A (11, F)
C (7, E)
D (8, E)
F
G (3, F)
B (4, F)
7
3
7
3
11
4
3
2
4
3
2
5
4
2
3
2
Examine nodes adjacent to E that are not permanent and update distances.
Identify the nearest node that is not permanent. This is labelled as permanent.

## Slide 44: 2nd Example of Dijkstra’s Algorithm
E (5, G)
A (11, F)
C (7, E)
D (8, E)
F
G (3, F)
B (4, F)
7
3
7
3
11
4
3
2
4
3
2
5
4
2
3
2
Examine nodes adjacent to C that are not permanent and update distances.
Identify the nearest node that is not permanent. This is labelled as permanent.

## Slide 45: 2nd Example of Dijkstra’s Algorithm
E (5, G)
A(10, D)
C (7, E)
D (8, E)
F
G (3, F)
B (4, F)
7
3
7
3
11
4
3
2
4
3
2
5
4
2
3
2
Examine nodes adjacent to D that are not permanent and update distances.
Identify the nearest node that is not permanent. This is labelled as permanent.

## Slide 46: 2nd Example of Dijkstra’s Algorithm
E (5, G)
A(10, D)
C (7, E)
D (8, E)
F
G (3, F)
B (4, F)
7
3
7
3
11
4
3
2
4
3
2
5
4
2
3
2
→ A = 10
→ D
→ E
→ G
F
→ B = 4
F
→ C = 7
→ E
→ G
F
→ D = 8
→ E
→ G
F
→ E = 8
→ G
F
→ G = 3
F

## Slide 47: Homework: Another example of Dijkstra’s Algorithm

## Slide 48: Homework: Another example of Dijkstra’s Algorithm - Results
Iteration | T | L(2) | Path | L(3) | Path | L(4) | Path | L(5) | Path | L(6) | Path
1 | {1} | 2 | 1–2 | 5 | 1-3 | 1 | 1–4 |  | - |  | -
2 | {1,4} | 2 | 1–2 | 4 | 1-4-3 | 1 | 1–4 | 2 | 1-4–5 |  | -
3 | {1, 2, 4} | 2 | 1–2 | 4 | 1-4-3 | 1 | 1–4 | 2 | 1-4–5 |  | -
4 | {1, 2, 4, 5} | 2 | 1–2 | 3 | 1-4-5–3 | 1 | 1–4 | 2 | 1-4–5 | 4 | 1-4-5–6
5 | {1, 2, 3, 4, 5} | 2 | 1–2 | 3 | 1-4-5–3 | 1 | 1–4 | 2 | 1-4–5 | 4 | 1-4-5–6
6 | {1, 2, 3, 4, 5, 6} | 2 | 1-2 | 3 | 1-4-5-3 | 1 | 1-4 | 2 | 1-4–5 | 4 | 1-4-5-6

## Slide 49: Centralised Routing
One routing table is kept at a “central” node
When a node needs a routing decision, it asks the central node
The central node must be able to handle large number of routing requests
Notes: With adaptive routing, routing tables can change to reflect changes in the network
Static routing does not allow the routing tables to change.
Static routing is simpler but does not adapt to network congestion or failures.

## Slide 50: Distributed Routing
Each node maintains its own routing table
No central node holding a global table
Somehow each node has to share information with other nodes so that the individual routing tables can be created
Individual routing tables may hold outdate information