## Slide 1: Computer Forensics 2
Introduction to Mobile Phone Forensics
Dr Diane Gan

## Slide 2: Introduction
Mobile phone investigations
Overview of services
Rules for processing a mobile phone
Tools
GSM Cellular Network
GSM File Structures
iPhone

## Slide 3
Everyone has at least one mobile phone
Harder to hide stuff on a mobile phone
Follow the ACPO guidelines
Identify the device
Isolate / extract / validate / report
Rules for mobile phones
  Process the hash values at the start
  Process the hash values at the end and compare
  If not equal then identify where data change occurred and document
  Must have at least 50% charge at the start of an investigation

## Slide 4: Logical Vs Physical Acquisition
Logical Acquisition
SMS; contacts (SIM and phone); chats; media; audio; cookies (mobile web sites)
Calendar – deleted and non-deleted next to each other
Call logs – outgoing and incoming
Contacts – lot of deleted entries + pictures
Use manual analysis / tools
Physical Acquisition
Physical = File system + deleted files
File system = logical all files + hidden files
E.g. Sqlite DB may contain deleted data and bluetooth logs
Like looking at hard drive – binary image
No unallocated space
Phone off – so no password issues

## Slide 5: Evidence from Mobile Devices
Can prove that someone was at a location when they say they were not
Military – posting pics – meta data and pic back ground
Found keyword search in iPhone 5 backup – rebuilt backup and got a complete copy of iPhone (backlite)
iPhones – can get image of IOS using software

## Slide 6: Overview of services
Define important acronyms for mobile phones
Overview how CDMA, GSM, iDEN and UMTS services work
Identify various locations where data may be stored on each type of phone
CDMA – Code Division Multiple Access
GSM – Global Systems for mobile Communication
iDEN – Integrated Digitally Enhanced Network
UMTS – Universal Mobile Transmission Service (3G)
        Uses wideband CDMA
Notes: CDMA - Uses a Spread-spectrum technique in which electromagnetic energy generated in a particular bandwidth is spread in the frequency domain, resulting in a signal with a wider bandwidth. Spread-spectrum techniques are used for a variety of reasons, including to establish secure communications, increase resistance to natural interference and jamming and prevent detection.
Spread-spectrum – energy generated in a particular bandwidth is spread in the frequency domain, resulting in a signal with a wider bandwidth. This is done to establish secure communications, increase resistance to natural interference and jamming and prevent detection. Each transmitter is assigned a code to allow multiple transmitters to use the same frequency channel at the same time. The CDMA protocol tags each part of multiple conversations with a specific digital code. The code enables the operating system to reassemble the jumbled calls at the base station using filters. This makes CDMA more efficient than Time Division Multiple Access (TDMA) because it allows more users per bandwidth.
GSM – Global Systems for Mobile Communication. Most popular standard for mobile phones in the world. Allows international roaming. Uses Subscriber Identity Module (SIM)cards which contain a user’s subscription information and phonebook. This allows the user to retain their information after switching handsets. Alternatively the user can change the SIM card. GSM is used on most 2G networks and uses “bursts”. This means that information is transferred based on time, as with TDMA. In 3G networks, GSM communication is based on the CDMA model, allowing GSM to be much more efficient.
iDEN – Integrated Digital Enhanced Network is a mobile telecommunications technology developed by Motorola. iDEN provides its users the benefits of a trunked radio and cellular telephone. This technology is not as efficient as CDMA based networks because only a small amount of conversations can occur at the same time in the same space. However, the radio or push-to-talk (PTT) technology allows you to use your cell phone like a walkie talkie radio, so the cellular network (towers) are not used.
Wideband Integrated Digital Enhanced Network (WiDEN) is a software upgrade developed by Motorrola for iDEN. WiDEN allows compatible subscriber units to communicate across 25 KHz channels combined, for up to 100 Kb/sec of bandwidth. The protocol is generally considered a 2.5G wireless cellular technology.

## Slide 7
4G Mobiles & Smartphones
networks and handsets introduced in 2010
Improvement is higher bit rates (up to 100 Mb/s) and easy roaming
5G Mobiles & Smartphones
Rolling out in 2020
10 times faster than 4G + lower cost
user is simultaneously connected to several existing wireless access technologies (3G, 2G, WiFi, WiLan, GPRS etc.)
6G Mobiles & Smartphones
Bandwidth 100 Gb/s expected

## Slide 8
Where is Data Stored
GSM and iDEN phones can store information in:-
  Handset
  SIM card
  Removable media
CDMA phone stores data:-
  Handset
  Removable media
Some CDMA phones also have a GSM SIM card to access both GSM and CDMA networks
Removable media can vary in size
Newer SDXC cards – up to 2 terrabytes (TB)

## Slide 9
Acronyms
CDMA
  ESN – Electronic Serial Number
  MEID – Mobile Equipment Identifier
  MIN – Mobile Identification Number
  MDN – Mobile Directory Number
GSM
  IMEI – International Mobile Equipment Identifier
  IMSI - International Mobile Subscriber Identity
  ICCID – Integrated Circuit Card Identifier
  MSISDN – Mobile Subscriber Integrated Services Digital Network number
  TMSI – Temporary Mobile Subscriber Identity
Equivalent to IMSI on GSM
Serial numbers for handset
The phone number
Serial number for handset
The phone number
Enter * # 06 #
indentify the subscriber
Notes: CDMA
  ESN – Electronic Serial Number – for the CDMA handset
  MEID – Mobile Equipment Identifier – both these are serial numbers to identify the CDMA handset. Often stored under the battery as well as internally
  MIN – Mobile Identification Number – like the IMSI on GSM
  MDN – Mobile Directory Number – these two numbers are used by the CDMA network.
  The MIN is like the IMSI on the GSM network. It identifies the subscriber on a CSMA network
  The MDN is what the someone dials to contact you – i.e. the phone number
GSM
  IMEI – International Mobile Equipment Identifier – serial number of the GSM equipment. Located on the label on the back side of the handset as well as internally in the devices memory. On some devices the IMEI can be located on the SIM card and on some USIM cards in the UK
  You can get this by pressing * # 06 # on the GSM device
  IMSI - International Mobile Subscriber Identity – the cellular network uses this to indentify the subscriber. It is not the phone number or the MSISDN of the handset – use the IMSI for getting billing information
  ICCID – Integrated Circuit Card Identifier – is the serial number of the SIM or USIM. It is the unique number utilised by the GSM network and it can identify information about the card itself such as country and network code

## Slide 10
Hardware Identification
IMEI – International Mobile Equipment Identifier
  unique number on handset - 15 or 17 digits
  Identifies GSM mobile phone on GSM network
  Finger print of mobile handset
Type Allocation Code | Serial Number | Checksum
01306300 | 229669 | 0
Identifies vendor & mobile device
Identifies specific device manufactured by vendor
Data integrity

## Slide 11
Essential Components
  The device
  Network subscriber (user)
1. SIM card structure
  ICCID – 19 or 20 digits
  Unique
  Major Issue ID (MII) > 89 for telecom
  Mobile Country Code (MCC)
  Issuer ID
  Individual Account ID
MII | MCC | Issuer ID | Acct No | Check Sum
89 | 602 | 021234 | 98765432 | 3
MCC | Country
602 | Egypt
Example SIM ICCID - 89602021234987654323
Subscriber Identifier

## Slide 12
2. IMSI – International Mobile Subscriber Identity
  14 or 15 digits
  Mobile country code (MCC)
  Mobile network code (MNC)
  Mobile subscriber identification number (MSIN)
  Going abroad – N/W looks up provider
  Provider checks if IMSI collides (country specific)
  Gives Temporary IMSI
MCC | MNC | MSIN
602 | 02 | 0123456789
Example IMSI = 602020123456789
MNC | Network
02 | Vodaphone
MCC | Country
602 | Egypt

## Slide 13
3. MSISDN – Mobile Subscriber ISDN
11 digit number
Country code (CC)
Number Planning Area (NPA)
Subscriber Number (SN)
You can also uniquely identify CDMA subscribers
CC | NPA | SN
1 | 973 | 5551212
NPA | Region
973 | Morristown, New Jersey
CC | Country
1 | USA
Example MSISDN = 19735551212

## Slide 14: Rules for processing a mobile phone
Recover all items – cables, SIMs, chargers, removable media
Isolate handset from the network
  Use a Faraday cage or bag
  Use an offline method – airline mode
  Create a forensics SIM clone
    Tools – Cellebrite, XRY, MFI Forensics SIM Cloner
Must have a charge of at least 50%
Process all media
  If the handset is off - process the media card / SIM card first
  If the handset is on – process media card in phone and when the acquire is complete process media card separately
Process physically and then logically
Notes: Make sure all items are recovered
grab everything – extra SIM cards and media cards may belong to other phones and could contain evidence
Isolate handset from the network
to ensure that no data is changed or overwritten
if you don’t have a faraday bag you can wrap it in aluminium foil (at least 3 wraps) – use airplane mode – use BitPim to place the phone offline (some software packages will boot it back into online mode – use bluetooth and WiFi connections
Charge the phone
at least 50% charge to complete an acquistion
If less the computer may not recognise the device connected to the USB
May not extract all the data correctly
Process all media
if the phone is on process the media with additional tools to get a bit-by-bit image of the media cards
Process physically and then logically
you want to retain the raw data of the physical acquistion because you can see if any changes have been made to the file system on that phone
When you process the device logically, follow the steps for the forensics process by hashing and rehashing
Note some Blackberry handsets encrypt data. If the data is processed outside the device, it will not be readable. In this case process the device first.

## Slide 15
If the phone is OFF
  Place your initials in the battery compartment and on the SIM
  Take pictures of the handset
    front and back
    serial number
    SIM card
    Battery off showing IMEI, ESN/MEID
  Remove the SIM card and any removable media
  Process SIM /Media card independently of the phone
  Isolate the phone from the network
  Turn on the phone
  Perform physical acquisition of the handset
  Perform logical acquisition of the handset (Hash and Rehash)
  Take screen shots and document everything
Notes: Must process the SIM card separately so that the entire file system can be processed using tools like SIMCon.
If there is a media card process this independently of the handset so that a bit-by-nit copy of the media can be made.

## Slide 16
If the phone is ON
  Isolate from the network – Faraday cage / airline mode
  Do NOT turn it off – it may be PIN protected
  Keep the phone alive
  Research the phone and decide what software to use
  Process the SIM card using logical software
  Extract the SIM card content
  Perform physical acquisition of the handset
  Perform logical acquisition of the handset
    Hash
    Rehash
  Take pictures of the handset
    front and back
    serial number
    SIM card
    After processing - battery off showing IMEI, ESN/MEID
Notes: If the phone has a SIM PIN, turning it off locks the phone and you will need the PUK code to recover it.
You will need the power cord to keep the phone alive without the battery power
When researching the phone a good source is www.numberingplans.com. This site contains information about phones that have been examined by other forensics examiners and the method used to process that phone.
Use logical software to locate and extract the ICC-ID and the IMSI so that you can create a forensic SIM clone. A SIM clone is useful if the phone is password protected and is turned off or the battery dies. You can replace the SIM and carry on processing the phone.

## Slide 17: Mobile to Landline
760-809-8925
SEND KEY
Master Switching Centre (MSC)
Public Switched Telephone Network (PSTN)
Checks Strongest Signal
call initiation
Routed to
Routed to land line
Confirms signal tone
Notes: The call is initiated. As the call travels into the network, it goes through the towers to find the strongest signal.
It is then routed to the Master Switching Centre (MSC). [It is also routed to two subsections – discussed later]
The call then goes to the public route switch (PSTN) and then to a land line or to another mobile on a different network.

## Slide 18
Mobile to Mobile
760-809-8925
SEND KEY
Master Switching Centre (MSC)
Public Switched Telephone Network (PSTN)
Checks Strongest Signal
call initiation
X
Notes: This scenario does not use the public switching centre (PSTN). Instead the call is routed just through the Master Switching Centre (MSC) – see next slide.

## Slide 19
The Mobile Station (MS) consists of:-
Mobile Equipment – ME – conduit to SIM
ME is uniquely identified by the IMEI
IMEI – International Mobile Equipment Identity number – serial number of phone
SIM card (Subscriber Identity Module)
  Acts like a key to the network
  Used to identify the subscriber to the system
  Secret keys for authentication (PIN and PUK)
  SIM contains –
    IMSI - International Mobile Subscriber Identity
    ICCID – Integrated Circuit Card Identification
Other useful user information – phone book, SMS, last numbers dialled, call history, etc.
Missed calls are not stored on the SIM
SIM
ME
Mobile
Station
Notes: While the mobile Equipment (ME) is the only part of the network seen by the user, it is actually anonymous to the network. The handset works as a container for and a conduit from the SIM. The ME’s radio transceiver, display and digital signal processors all serve the SIM. Without the SIM the handset can not connect to or operate on the network.
The IMEI provides a way to uniquely identify the handset as required.
The IMEI and the IMSI are independent of each other.
Files on the SIM
Identifies the subscriber – IMSI
Secret key for authentication
  KI – used during the authentication process
  KC – ciphering key
  PIN - personal identification number
  PUK – personal/PIN unblocking number
Other useful user information – phone book, SMS, last numbers dialled, call history, etc.
Missed calls are not stored on the SIM
Most have evidentiary value
  Most provide network rather than subscriber data

## Slide 20: GSM Cellular Network
SIM
ME
Mobile
Device
BTS
BTS
BSC
BSC
MSC
HLR
VLR
EIR
AuC
PSTN PSPDN
Base Station Subsystem
Network Subsystem
UM
Abis
Abis
Mast
Mobile Switching Centre
base transceiver station
base station controller
equipment register
Notes: Mobile Device – Mobile Equipment (ME) + SIM used by the subscriber
Base Station Subsystem – cell tower that communicates with the mobile equipment
BTS – base transceiver station - Handles the radio link protocols (to ME)
BSC – base station controller - Manages the radio resources for one or more BTSs
  Handles radio-channel setup, frequency hopping and handoffs
Network Subsystem – Mobile Switching Centre (MSC) – acts like a router and the data bases used to authenticate with the network
HLR – home locator register (where billing is) – stores your data now – only one of these – HLR is eventually updated with info from the VLR
HLR contains
  Subscribers home address
  Subscribers International Mobile Subscriber Identity (IMSI)
  Subscribers phone number
  SIM card’s Integrated Circuit Card Indentifier (ICCID)
  GSM services that the subscriber has requested or been given
VLR – visitor locator register (geographic – i.e. current location) – can have many of these but you can only use one based on geography. E.g. The HRL for a subscriber from Kent is located in Kent. If this subscriber travels to Yorkshire, Tee-side and then Scotland, then there will be a VLR in each location.
EIR – equipment register (stolen etc) – if it has been stolen then it will not authenticate
AuC – authentiticator centre
Abis – the interface between the base station and base station controllers, which allows operation between components made by different suppliers
Um – air interface from the ME to the base station subsystem

## Slide 21: Mobile Switching Centre
MSC – mobile switching centre
  Is the router of the system
  Performs telephony switching functions
  Controls transmission between
    Cellular to cellular / Cellular to land line / Cellular to Internet
HRL – home location register – all admin info for each subscriber
VLR – visitor location register –
  Contains selected info from the HLR nec. for call control
  Temporary DB that holds info about subscribers who have roamed into it’s area
  Includes
    TMSI (temporary mobile subscriber number)
    Subscribers phone number
    GSM services they are permitted to access
    Current location of handset
    HLR address of the subscriber
Notes: The VLR (visitor locator register) and the HLR (home location register) are just databases
HLR contains
Subscribers home address
Subscribers International Mobile Subscriber Identity (IMSI)
Subscribers phone number
SIM card’s Integrated Circuit Card Indentifier (ICCID)
GSM services that the subscriber has requested or been given
Information is sent to the HLR from the VLR and is updated based on specific network protocols.
VLR – visitor locator register (geographic – i.e. current location) – can have many of these but you can only use one
There is only one HLR but there can be many VLRs for each subscriber, because this is based on geography.
E.g. The HRL for a subscriber from Kent is located in Kent. If this subscriber travels to Yorkshire, Tee-side and then Scotland, then there will be a VLR in each location.

## Slide 22
Equipment Identity Register - EIR
Std GSM network element
Enables a mobile network to check the type and serial number of a mobile device
  White-listed = contains all known and valid IMEI numbers
  Grey-listed = contains all IMEI of devices of dubious status
  Black-listed = contains all defective and stolen devices
Authentication Centre – secure DB
  Handles authentication and encryption keys
  If successful the HRL is allowed to manage the SIM
Notes: EIR – equipment register (stolen etc) – if it has been stolen then it will not authenticate
IMEI – International Mobile Equipment Identifier

## Slide 23
Authentication
AC authenticates each SIM card as it tries to connect to the network
Occurs when the phone is switched on
Authentication involves
  TMSI – temporary mobile subscriber identity
  ICCID – integrated circuit card identifier
Encryption key is generated
Some kind of security –
  ki – random number obtained from the cipher key (transmitted)
  Kc – ciphering key
Given a secret key – one copy stored in SIM and one copy in the AuC
Notes: Authentication involves
  TMSI – temporary mobile subscriber identity
  ICCID – integrated circuit card identifier
Some kind of security – ki – random number obtained from the cipher key (transmitted)
        Kc – ciphering key
If encryption fails then no services are available from the SIM + device
Each subscriber has a secret key (KI). One copy is stored in the SIM and the other is in the AuC.
When the phone authenticates, the AuC generates a random number (RAND) which it sends to the handsets. The mobile and the AuC take the random number with the KI and using an algorithm, they generate a unique number. This is returned to the AuC and if it matches the number in the AuC then the subscriber is authenticated.

## Slide 24
GSM Authentication
HLR
AuC
IMSI
KI
Rand
KI
Rand
Result
A3
A3
= network result
Read off SIM card
128 bits Rand + 32 bits SResp + 64 bit session key Kc
Your mobile never authenticates the GSM network, which enables false provider attacks to occur
Signs in
Signed Response
BTS
MSC
SIM Result
TMSI
Notes: GSM Authentication
The KI is read off the SIM card. It changes each time and is written back to the phone from the server. A3 is the algorithm used – also uses A8 and A5.
The Mobile Switching Centre (MSC) requests the HLR to supply “five triples” using the A8 algorithm. These contain a 128 bit random challenge (Rand), a 32 bit matching Signed Response (SRES) and a 64 bit ciphering key used as the session key (Kc).
The MSC send the Rand to the BTS, which relays it to the mobile. The mobile in turn encrypts the Rand with its KI key using the A3 algorithm and sends this Signed Response back to the MCS which verifies it. At the same time the mobile uses the Rand again to create a session key (Kc) using its KI and the A8 algorithm. The mobile passes the Kc on to the BTS. The BTS having received a Kc session key from the MSC and confirms it with the Kc received from the MS. The wireless channel is now encrypted using the A5 algorithm
Same session key (Kc) is used so long as the MSC does not authenticate the mobile phone again
The session key is located on the SIM in location GSM G1500 dedicated files
HLR – home locator register (where billing is) – stores your data now – you only have one of these – HLR is eventually updated with info from the VLR
VLR – visitor location register – (your current location) – can have many of these
AuC – authenticator centre
BTS – base station transceiver
MSC - Mobile Switching Centre
TMSI - temporary mobile subscriber identity

## Slide 25: GSM File Structures
Master File
Dedicated File
Elementary File
MF
3F 00
DF
7F xx
DF
7F xx
DF
5F xx
Elementary File 2F xx
Elementary File 4F xx
Elementary File 6F xx
Elementary File 6F xx
Elementary File 6F xx
C:\ or root
folder
files
MF – master file
DF1 – 1st level DF
DF2 – 2nd level DF
EF – elementary files
Notes: Master File – equivalent to C:\ drive
Dedicated File - a folder
Elementary File – a file

## Slide 26
Master File [3F 00]
Unique mandatory file
Contains access conditions that the handset uses to communicate with a service provider
Contains Dedicated and Elementary files (optional)
Dedicated File [7F xx]
File containing
  Access conditions
  Other DFs and Elementary Files
Elementary Files
Access conditions e.g. PIN
Data and no other files

## Slide 27
Elementary Files (EFs)
Made up from header and a body
Contain data
Three main types
  Transparent – store non-repetitive data
  Linear fixed – all files have same length
  Cyclic – files stored in chronological order (accumulated call meter, last number dialled)
Missed calls are not stored on the SIM

## Slide 28
Transparent EF
  stores non-repetitive data
  Has no fixed structure
  First byte has relative address - 00 00
  Examples
    ICCID
    IMSI
    Language pref
    Ciphering key (Kc)
    PLMN - public land mobile network
    HPLMN - home PLMN
    SIM Service Table
Notes: PLMN – public land mobile network
HPLMN – home PLMN
IMSI - International Mobile Subscriber Identity - what someone dials to contact you – i.e. the phone number
ICCID Integrated Circuit Card Identifier – is the serial number of the SIM or USIM. It is the unique number utilised by the GSM network and it can identify information about the card itself such as country and network code

## Slide 29
Linear fixed EF – all files have same length
  Sequence of records e.g. Phone book
  First record is Record number 1
  Length of each record is stored in EF header
  Currently max is 255 linear fixed EFs with max 255 bytes in each
To access a linear fixed EF
  Use the record number
  If the pointer is not set - use Next or Previous mode
  If the pointer is set – can perform an action on the record, or the next or previous one
  Identify a record using a pattern seek
    Forward from the beginning
    Forward from the record following (unless on the last record)
    Backward from the end of file or from the current record

## Slide 30
Cyclic EF
Files are stored in chronological order
Fixed number of records with the same fixed length
Limited to 255 total bytes and 255 total cyclic EFs
When all records have been used, the next data overwrites the oldest data
Link between the last record and the first
Examples - accumulated call meter (ACM)
last number dialled (LND)

## Slide 31
MF
3F 00
DF - GSM
7F 20
DF - Telecom
7F xx
DF
5F xx
EF - ICCID
2F E2
10 bytes
Elementary File 4F xx
EF-SMS
6F xx
EF-MSISDN
6F xx
EF-IMSI
6F 07
EF-ADN
6F xx
EF-LND
6F xx
EF-kc
6F xx
EF-LOCI
6F xx
EF-TMSI
6F xx
Master File
Dedicated File
Elementary File under Master File
Elementary Files – under a Dedicated File 6F xx
Notes: EFs File Type
EF-ICCID Transparent – stores nonrepetitive data
EF-IMSI Transparent – stores nonrepetitive data
EF-kc
EF-LOCI
EF-TMSI
EF-MSISDN
EF-ADN
EF-LND cyclic – stored in chronological order
TF-SMS linear fixed – all files are the same length
Dedicated File [7F xx]
Found on the first and second levels in the SIM file structure
First level DFs
  DF – TELECOM
  DF-GSM
  DF_DCS1800 – contains Telecom service features
Second level DFs are children of DFs (e.g. DF-GSM)

## Slide 32
EF- ICCID
Elementary File under the Master File
2F E2
10 bytes
Identifies the SIM
Read – ALW = always
Update – NEV = never
Deactivate – ADM = admin
Activate - ADM
EF_ICCID
DF-GSM
DF-DCS1800
DF-Telecom
MF

## Slide 33
EF - LOCI
Contains location information
Last location where phone was powered down
Updated as the phone moves from one location to another
File size = 11 bytes
File structure = Transparent
Byte 1-4 is the TMSI
Bytes 5-9 LAI
Byte 10 is TIMSI time
Byte 11 – location update status
TMSI – Temporary Mobile Subscriber Identity
EF_ICCID
DF-GSM
EF – IMSI
EF – Kc
EF – ACM
EF – LOCI
EF – PLMN
EF - FPLMN
..
Notes: EF-LOCI
Contains information about the last location where the phone was successfully powered down.
Also contains the TMSI
Can decipher this information to obtain the last location.
Be aware that if the phone is not powered down correctly (such as battery removed or phone is damaged) then the location is not stored on the SIM card.

## Slide 34
EF-IMSI
International Mobile Subscriber Identity
File ID = 6F07
File size = 9 bytes
File structure = Transparent
Byte 1 contains the length
Bytes 2-9 contain the data
Stores
  Mobile Country Code
  Mobile Network Code
  Mobile Subscriber Identity Number (MSIN)
IMSI is used to identify the user on the network
EF_ICCID
DF-GSM
EF – IMSI
EF – Kc
EF – ACM
EF – LOCI
EF – PLMN
EF - FPLMN
..
Notes: Go to www.numberingplans.com
Enter the IMSI – you will get the country code as well as the network code
More information on IMSIs in document 31102_900.pdf

## Slide 35
EF- PLMN
Public Land Mobile Network
File ID 6F 30
Consists of
  Mobile Country Code (MCC)
  Mobile network Code (MNC)
At least 8 PLMNs are on the SIM card
Networks available for access
Listed in priority
Updated over the air – important for tracking a suspect as the PLMN changes
EF_ICCID
DF-GSM
EF – IMSI
EF – Kc
EF – ACM
EF – LOCI
EF – PLMN
EF - FPLMN
..

## Slide 36
DF-Telecom
Contains the majority of the user data
Newer phones may store info on the handset
Depends on the phone
SMS – short message service
  Received SMSs (30 slots)
  File ID = 6F3C
  Users can select a different location
  Can’t have incoming calls on SIM only outgoing
EF_ICCID
DF-GSM
DF-Telecom
EF – ADN
EF – FDN
EF – SMS
EF - MSISDN
EF – ..
EF – LND
EF - ..
..

## Slide 37
DF-Telecom (contd)
ADN – abbreviated dialed numbers
LND – last numbers dialed
MSISDN – Mobile station ISDN
255 slots for storing phone numbers
  File ID = 6F3A
  When numbers are deleted the slot is filled with FF16
  Allocated in sequence – so you can tell if one is deleted
  Most phone can store 10 last-dialled numbers File ID = 6F44
  Manufacturers do not use this – use calling log instead
  SIMs do not store received call data
  MSISDN - File ID = 6F40 – a phone can have more than one
EF_ICCID
DF-GSM
DF-Telecom
EF – ADN
EF – FDN
EF – SMS
EF - MSISDN
EF – ..
EF – LND
EF - ..
..
Notes: Most phones have up to 255 slots dor storing phone numbers

## Slide 38
SMS
Broken down in to 3 files:-
You can NOT retrieve slack if a SMS is overwritten
This also applies to Contacts and Call logs
File | Purpose | Size
SMS | The text messages | 1 to 176 bytes
SMSP | Message parameters | variable
SMSS | Status of the message | variable
Value of Status Byte | Interpretation
00000000 | Unused (available)
00000001 | Mobile terminated message, read
00000011 | Mobile terminated message, unread
Notes: SMS has 3 file types:
SMS – stores the text messages
SMSP – message parameters – can be variable length
SMSS – has the status of the message
Deleting a text message on a SIM card only changes the first byte.
If a 140 byte message is marked as deleted and then it gets overwritten by a 10 byte message, you would expect to be able to retrieve the slack, but you can’t. Each message write 140 bytes regardless and fills any bytes leftover with Fs.

## Slide 39
Status | Transport Protocol Data Unit (TPDU)
1 byte | 2 – 176 bytes
TPDU
Consists of:-
  ISDN number of the SMS service centre
  ISDN number of the sender
  Date and time (in secs) that msg was received by service centre
  Message itself
Encoding varies – most common is 7 bit packed
Optimised for streaming onto the SIM
Unused bytes will contain FF

## Slide 40: PM Files
PM stands for permanent memory
PM file structure uses keys
Some content such as IMSI is actually flipped
example 98 becomes 89
Use the MFI HEX Assistant to flip the nibble
In SMS messages some phone numbers have the digits flipped throughout the entire number
At key [58] there are two sub-keys (1 and 2)
Once the hex is decoded – name and phone number

## Slide 41
Keys of interest:-
[5] IMEI
[13] Banner
[35] Security Code
[58] Contacts for this specific phone
[59] Dialled
[60] Missed
[61] Received
[117] ICCID
[127] and [39] URLs
[150] SMS
[159] Media (sound, GIFs, JPEGs)

## Slide 42
PIN – personal identification number
Locks the SIM
Protects SIM even when put into another phone
3 failed attempts and the SIM is blocked
To unlock you need the PUK
PUK – PIN Unblocking Key
8 digit code
10 attempts and then the SIM is permanently blocked
Entering the PUK forces user to enter a new PIN
User can reset the PUK
Newer SIM cards have a PIN Code 2
Controls access to the advanced features of the phone

## Slide 43
Important facts about PIN/PUK
PIN protects SIM
PIN is set by the manufacture
PIN is 4 digit code
You only have 3 attempts to enter the PIN
To bypass a blocked SIM you need the PUK
PUK is set by the manufacture
Have 10 attempts the correctly enter the PUK
If you fail the PUK attempt counter can never be reset
Both PIN and PUK can be changed by the user
Current forensics issues – new iPhone’s 5 PIN lock

## Slide 44: Cloning SIM cards
Why would you want to create a Forensic SIM clone?
The handset may not have a SIM card
Request ICCID and IMSI from the carrier using the IMEI
Why not just put a new SIM card in?
The phone will delete its call history
Other things that can be deleted are call logs and other useful data (in 99.9% of phones)
Also want to preserve the original evidence
Can get the ICCID and the IMSI from the handset
Place these onto the SIM clone
Fools the handset into recognising its SIM card
Then proceed with the investigation
Notes: If we do have the SIM card, we may still want to create a clone
Do we want to copy all the files from the original SIM?
Negates the required network isolation
It is illegal to connect with a cloned SIM card using another subscriber’s information
The cloned SIM will have no information to connect to the network
Final reason for creating a cloned SIM card is to preserve the original evidence
Read the original SIM card using forensics tools
Use the copy to investigate the handset
Thereby preserving the evidence

## Slide 46: iPhones
iPhone forensics is relatively new
Most popular phone on the market
Not finalised – legality and standards
Use a Faraday Shield when seizing an iPhone
Current phones come with large storage
Has GPS capabilities – significant for an investigation
Get an image rather than examining live phone
Three methods:-
  View the iTunes Sync on a host computer (logical image)
  Hacking into the iPhone
  Disassembling the iPhone
/Users/username/Library/Application Support/ MobileSync/Backup/
Notes: Using the iTunes Sync program you can make a logical image of the iPhone data. This will not include any deleted files or folders.
Problem – if you can’t locate the host system then you will not get all of the data. For example if the user has put in movies or music (binary data) on their system, you will not be able to retrieve these due to the Digital Rights Management (DRM) features.
If you sync the phone to a different computer then data will be lost.

## Slide 47
Jailbreaking
Most mobile devices have a read-only file system
Vendors want to prevent users from changing to critical areas
Opening these areas is called jailbreaking or rooting
Changes the file system from read only to read/write
Allows unauthorised software to execute on the device
Bypasses the handset network lock
Full read/write access to the entire memory of the device
Notes: Jailbreaking – used to gain root access by the forensics community
The Physical image may not be admissible in court

## Slide 48
Problems
Altering data on the OS partition violates forensics integrity
Could compromise the device’s operation
Only way to reverse this is to do a complete system restore – again violating the forensic integrity of the device
Installing a new vers of the iOS will re-flash the OS partition
The fstab file will no longer show the partition as read/write
For an Andriod device the only evidence the device has been rooted may be a binary named “su” – found in /system/xbin or in system/bin

## Slide 49: Summary
Understand how a mobile device sends information to the network
Understand SIM card structures
Understand the data types
Define the file structures, SIM card areas
Appreciate SIM card security
Overview of iPhones